## Slide 1: Mechanisms and Robotics DE ES DM ZG561
Lecture - 4
Dr. Glynn John
Mechanical Engineering

## Slide 2: Robot Kinematics
Forward kinematics
Rotation
Translation
Post-multiplication Vs. Pre-multiplication
Homogeneous Transformation
Introduction to Denavit – Hartenberg Parameters
θ – r manipulator

## Slide 3: Find the dof

## Slide 4: Find the dof
N= 8
J = 9
Fi = 15
Dof = 3

## Slide 5: Find the dof

## Slide 6: Find the dof
Each parallelogram linkage has one degree of freedom of motion, so that each leg of the Delta robot is kinematically equivalent to an RUU chain.
L= 8
J = 9
Fi = 15
Dof = 3

## Slide 7
Home Work

## Slide 8: Home Work

## Slide 10: Direct Kinematics
A robotic manipulator can be modelled as a chain of rigid bodies called links.
The links are interconnected to one other by joints.
The objective is to control both the position and the orientation of the tool in three-dimensional space.
In order to program the tool, we must formulate the relationship between the joint variables and the position and the orientation of the tool.
This is called the Direct Kinematics problem.

## Slide 11: Kinematic Parameters
Joint Parameters
Link Parameters

## Slide 12: Coordinate Systems – Right Handed, Left Handed
Directions of Positive X Y Z axes

## Slide 14: Coordinate Systems
Anticlockwise rotation is positive when seen from the opposite direction of the arrow head
Directions of Positive X Y Z rotations

## Slide 15
Rotation Matrices

## Slide 16
Fundamental rotation matrices for rotation about x axis y axis and z axis are given as follows.
Rotation Matrices

## Slide 17
Find the result of rotating the point [7,2,5]T through 90° in the positive direction about the z-axis.
Problem 1

## Slide 18
Find the result of rotating the point [7,2,5]T through 90° in the positive direction about the z-axis.
Problem 1 - Solution

## Slide 19
Translation of a Point

## Slide 20
The matrix is divided into four sub-parts and these sub-matrices are as shown below.
Here is rotation matrix.
is translation matrix.
is a non-zero scaling factor.
is a perspective vector.
Homogeneous Transformation Matrices

## Slide 21
Homogeneous Transformation Matrices
When we want to describe a generalized transformation by a single matrix that combines the effects of translation and rotation, we define a vector by adding 1.

## Slide 23
Composite Rotations
If the mobile coordinate frame M is to be rotated by an amount ϕ about the Kth unit vector of the fixed coordinate frame F, then pre-multiply R by Rk(ϕ)
If the mobile coordinate frame M is to be rotated by an amount ϕ about its own Kth unit vector, then post-multiply R by Rk(ϕ)
Post-Multiplication Vs. Pre-Multiplication

## Slide 24
Find the result of rotating the point [7,2,5]T through 90° in the positive direction about the z-axis followed by a rotation of 90° about the x-axis, followed by a translation of (4,5,6).
Problem 2

## Slide 25
Find the result of rotating the point [7,2,5]T through 90° in the positive direction about the z-axis followed by a rotation of 90° about the x-axis, followed by a translation of (4,5,6).
Solution:
Trans(4,5,6)*Rotx(90)*Rotz(90)*[7,2,5]T
Ans:
Problem 2 - Solution

## Slide 27
Denavit and Hartenberg (1955) proposed a systematic notation scheme for assigning right handed orthonormal coordinate frames, one to each link in an open kinematic chain of links.
Once these coordinated frames are assigned, transformations between adjacent coordinate frames can be represented by a single standard 4X4 homogeneous coordinate transformation matrix.
Denavit - Hartenberg Representation

## Slide 29
The Denavit-Hartenberg (D-H) framework is a method for assigning frames of reference to a serial robot arm constructed of sequential rotary (and/or translational) joints connected with rigid links.
If the robot arm is imagined at any fixed time, the axes about which the joints turn are viewed as lines in space.
In the most general case, these lines will be skew, and in degenerate cases, they can be parallel or intersect.
In the D-H framework, a frame of reference is assigned to each link of the robot at the joint where it meets the previous link.
The z-axis of the ith D-H frame points along the ith joint axis.
Since a robot arm is usually attached to a base, there is no ambiguity in terms of which of the two (+-) directions along the joint axis should be chosen, i.e., the “up” direction for the first joint is chosen.
Since the (i + 1)st joint axis in space will generally be skew relative to axis i , a unique x-axis is assigned to frame i, by defining it to be the unit vector pointing in the direction of the shortest line segment from axis i to axis i + 1.
This segment intersects both axes orthogonally. In addition to completely defining the relative orientation of the ith frame relative to the (i − 1)st, it also provides the relative position of the origin of this frame.
Denavit-Hartenberg (D-H) framework

## Slide 30
Denavit-Hartenberg (D-H) framework

## Slide 31: 2 dof manipulator – Forward Kinematics

## Slide 32: 2 dof manipulator – Forward Kinematics

## Slide 36: THANK YOU
References:
Industrial Robotics - Mikell P. Groover
Industrial Robotics Computer Interfacing and Control – Wesley E. Snyder
Fundamentals of Robotics – Robert Schilling
Introduction to Robotics: Analysis, Control, Applications, 2ed - Saeed B. Niku
Modern Robotics – Park and Lynch